## Slide 1: 使用 Cisco IOS NetFlow 進行網路裝置管理
Notes: Developed and patented by Cisco in 1996, NetFlow is now the primary network accounting technology in the industry. It answers questions regarding IP traffic such as:
Who are the top users?
How long are the users on the network?
What Internet sites do they use?
Where do the users go on the network?
What percentage of traffic do they use?
What applications do they use?
What are the user usage patterns?
In other words, NetFlow provides a detailed view of network behaviour.
This lesson covers the following exam topics:
Troubleshooting
Utilize netflow data
Monitor NetFlow statistics

## Slide 2: 目標
完成本課程時，你將能符合這些目標：
說明 NetFlow 的目的
說明 NetFlow 的架構
在 Cisco 裝置上配置並查驗 NetFlow

## Slide 3: NetFlow 概述
NetFlow 是一個用來收集 IP 流量資訊的應用
來自 NetFlow 的報表像電話費帳單
NetFlow 啟用下列 :
  - 測量誰使用網路資源
  - 依資源使用計量及收費
  - 使用測量資訊進行有效的網路規畫
  - 使用測量資訊來客制應用和服務
Notes: NetFlow is a Cisco IOS application that provides statistics on packets flowing through the routing devices in the network. It is emerging as a primary network accounting and security technology.
Cisco IOS NetFlow efficiently provides a key set of services for IP applications, including network traffic accounting, usage-based network billing, network planning, security, DoS monitoring capabilities, and network monitoring.
NetFlow technology creates an environment in which you have the tools to understand how network traffic is flowing. To use an analogy from the telephone industry, NetFlow is like a phone bill, from which you can learn who is talking to whom, how frequently, how long, and so on.
NetFlow is completely transparent to the existing network, including end stations and application software, and network devices such as LAN switches. Also, NetFlow capture and export are performed independently on each internetworking device. NetFlow does not need to be operational on each router in the network.
NetFlow is important for service providers and enterprise customers because it helps address four key requirements:
- Efficiently measuring who is using which network resources for which purpose
- Accounting and charging back according to the resource utilization level
- Using the measured information to do more effective network planning so that resource allocation and deployment are well-aligned with customer requirements
- Using the information to better structure and customize the set of available applications and services to meet user needs and customer service requirements

## Slide 4: NetFlow 概述 (續)
NetFlow 收集器上的分析範例:
顯示最大流量的流出者，流入者，協定和更多
Notes: There are several NetFlow collectors and analyzers available on the market. These tools enable you to analyze the traffic on your network by showing the top talkers, top listeners, top protocols, and more. You can see the types of traffic (web, mail, FTP, peer-to-peer, and so on) that are on the network, as well as which devices are sending and receiving most of the traffic. Collecting data provides you with forensic-level telemetry on top talkers, top hosts, and top listeners. And because data is preserved over time, you will be able to analyze network usage trends.
Based on the usage of NetFlow analyzers, you will be able to identify the following:
- The major users of the network
- The websites that are routinely visited and what is downloaded
- Who is generating the most traffic
- If you have enough bandwidth to support mission-critical activity
- Who is using excessive bandwidth

## Slide 5: NetFlow 概述 (續)
NetFlow 元件：
  - 啟用 NetFlow 的網路裝置
  - NetFlow 收集器
  NetFlow 裝置產生 NetFlow 匯出的紀錄，並由 NetFlow 收集器收集. 它也處理 NetFlow 資料並透過它的圖型人機介面提供結果
NetFlow-Enabled 路由器
NetFlow Collector
Notes: NetFlow components include the following:
- Network devices that are configured for NetFlow
- NetFlow Collector, which receives NetFlow information from network devices
Network devices collect IP traffic statistics on interfaces where NetFlow is configured. Network devices then export these statistics as NetFlow records to a central server that runs NetFlow Collector software. The Collector also performs traffic analysis.

## Slide 6: NetFlow 概述 (續)
Cisco 定義流量為一個帶有七項相同值的單向封包序列:
  - 來源 IP 位址
  - 目的 IP 位址
  - 來源埠編號
  - 目的埠編號
  - 第三層協定類型
  - 服務類型
  - 輸入邏輯介面
Notes: A NetFlow network flow is defined as a unidirectional stream of packets between a given source and destination. The source and destination are each defined by a network layer IP address and transport layer source and destination port numbers.
A flow is defined by the combination of seven key fields, which define a unique flow. If a packet has one key field that is different from another packet, it is considered to belong to another flow. Flows are stored in the NetFlow cache.
Note ToS is a field in the IP header. It is used as a quality of service (QoS) mechanism to mark IP packets with different priorities in
order to receive different treatment in terms of throughput, reliability, and latency.

## Slide 7: NetFlow 架構
路由器收集資料
流量收集軟體:
  - 流量紀錄接收 (UDP)
  - 資料量的減少和過濾
用來以繪圖方式顯示資料的網路流量分析軟體
Notes: The purpose of FlowCollector is to grab flow export data from multiple routers, filter and aggregate the data according to the policies of the customer (that is, keep the data that you want and discard the rest), and store this summarized or aggregated data instead of raw flow data to minimize disk space consumption. The data is written to a disk at specified intervals in flat files. The customer may run multiple collection schemes or threads concurrently; for example, customers who want data both for planning and for billing may want to store different “cuts” of the data to support these applications via different aggregation schemes.
FlowCollector passively listens to specified UDP ports to receive and process exported NetFlow datagrams. The FlowCollector application provides a high-performance, easy-to-use solution that scales to accommodate consumption of NetFlow export data from multiple devices in order to support key flow-consumer applications, including accounting, billing, and network planning and monitoring.
FlowAnalyzer provides the means to do near real-time visualization and analysis of recorded and aggregated flow data. You can specify the router, the aggregation scheme, and the time interval in which you wish to view and then retrieve the relevant data. You can then sort and visualize the data in a manner that makes sense for the users (with bar charts, pie charts, or histograms of the sorted reports). The data can then be exported to spreadsheets such as Excel for more detailed analysis, trending, reporting, and so on.
Cisco no longer supports its own specific Flow collection/analysis software. Other companies offer free or commercial flow collection/analysis software.
See these links:
http://www.cisco.com/en/US/prod/iosswrel/ps6537/ps6555/ps6601/networking_solutions_products_genericcontent0900aecd805ff72b.html
http://www.cisco.com/en/US/prod/iosswrel/ps6537/ps6555/ps6601/networking_solutions_products_genericcontent0900aecd805ff728.html

## Slide 8: NetFlow 配置
配置 NetFlow 資料擷取
配置 NetFlow 資料匯出
配置 NetFlow 資料匯出版本
查驗 NetFlow, 它的運作，和統計
Notes: To implement NetFlow on a router, you must do the following:
Configure NetFlow data capture: NetFlow can capture data from ingress (incoming) and egress (outgoing) packets.
Configure NetFlow data export: You need to specify the IP address or hostname of the NetFlow collector and the UDP port that the NetFlow collector listens to. Optionally, you can specify an interface to use for the source IP address of the packet sent to the collector.
Configure NetFlow data export version: You can specify the version of NetFlow data export format.
Verify NetFlow, its operation, and statistics: After you have configured NetFlow, you can analyze the exported data on a workstation running an application such as NetFlow Collection Engine or using several show commands on the router itself.
Note Be aware that NetFlow consumes additional memory. If you have memory constraints, you can preset the size of the NetFlow cache so that it contains a smaller number of entries. The default cache size depends on the platform.

## Slide 9: NetFlow 配置 (續)
R1(config)# interface GigabitEthernet0/0
R1(config-if)# ip flow ingress
R1(config-if)# ip flow egress
R1(config-if)# exit
R1(config)# ip flow-export destination 10.1.10.100 9996
R1(config)# ip flow-export version 9
在路由路 R1 上配置 NetFlow
Notes: Configuration of NetFlow is based on the following commands:
ip flow {ingress | egress}
Enables NetFlow on the interface. Captures traffic that is being received or being transmitted by the interface.
ip flow-export destination ip-address udp-port
IP address of the workstation to which you want to send the NetFlow information and the number of the UDP port on which the workstation is listening for this input. UDP port 9996 is commonly used for NetFlow.
ip flow-export version version
Specifies the version format that the export packet uses.
The figure shows configurations for NetFlow data capture and data export to NetFlow collector with IP address 10.1.10.100, where you can analyze the exported data.
Traffic that is being either received or transmitted by the GigabitEthernet 0/0 interface is captured using the ip flow command. Captured NetFlow information is then sent to the collector with IP address 10.1.10.100 on UDP port 9996. The ip flow-export version command specifies that the export packet uses the version 9 format.
Note NetFlow exports data in UDP in one of five formats (1, 5, 7, 8, and 9). Version 9 is the most versatile data export format but is not backward compatible with version 8 or version 5.

## Slide 10: NetFlow 配置 (續)
顯示 NetFlow 是否在介面啟用
R1# show ip flow interface
GigabitEthernet0/0
ip flow ingress
ip flow egress
R1# show ip flow export
Flow export v9 is enabled for main cache
export source and destination details :
VRF ID : Default
Destination(1) 10.1.10.100 (9996)
Version 9 flow records
43 flows exported in 15 udp dategrams
顯示 NetFlow 資料 匯出的狀態和統計
Notes: You can use the show ip flow interface command to verify if NetFlow is enabled on an interface. In the example, NetFlow is enabled in the ingress and egress directions on the GigabitEthernet0/0 interface.
Use the show ip flow export command to verify the status and statistics for NetFlow accounting data export. In the example, the configured destination for NetFlow export is 10.1.10.100 using UDP port 9996. The version of the configured flow export is 9.

## Slide 11: NetFlow 配置 (續)
R1# show ip cache flow
<output omitted>
IP Flow Switching Cache, 278544 bytes
2 active, 4094 inactive, 31 added
6374 ager polls, 0 flow alloc failures
Active flows timeout in 30 minutes
Inactive flows timeout in 15 seconds
IP Sub Flow Cache, 34056 bytes
2 active, 1022 inactive, 31 added, 31 added to flow
0 alloc failures, 0 force free
1 chunk, 0 chunks added
last clearing of 統計 00:49:48
Protocol Total Flows Packets Bytes Packets Active(Sec) Idle(Sec)
-------- Flows /Sec /Flow /Pkt /Sec /Flow /Flow
TCP-Telnet 19 0.0 19 58 0.1 6.5 11.7
TCP-WWW 14 0.0 8 202 0.0 0.0 1.5
TCP-other 2 0.0 19 98 0.0 2.2 8.9
<output omitted>
SrcIf SrcIPaddress DstIf DstIPaddress Pr SrcP DstP Pkts
Gi0/1 172.16.1.100 Gi0/0 10.2.23.105 01 0401 0017 1341
顯示 NetFlow 計量統計的摘要
Notes: You can use the show ip cache flow command to display a summary of NetFlow statistics on a Cisco IOS router. Using this command, you can see which protocols use the highest volume of traffic and between which hosts this traffic flows.
The example shows a summary of NetFlow statistics on the R1 router. Note that the destination port is hex 17, which is equal to decimal 23, the well-known TCP port for Telnet services.

## Slide 12: 摘要
NetFlow 提供流經網路上路由裝置的封包統計。
NetFlow 配置部分包括配置資料擷取和配置資料匯出。